## Slide 1: Communication protocols / networking
Lecture 7-8

## Slide 2: IoT network protocols
Most common IoT Network Protocols are:
MQTT
DDS
XMPP
Bluetooth
WiFi
Cellular
LoRaWAN

## Slide 3: MQTT (Message Queue Telemetry Transport)
MQTT is a lightweight protocol for sending simple data flows from sensors to applications and middleware. It uses a subscribe/publish system, where a device "subscribes" to a “topic” with the specific information of your interest, and then receives the information whenever a device publishes data concerning this topic. The protocol includes three components: subscriber, publisher and broker. The publisher collects data and sends it to subscribers. The broker tests publishers and subscribers, checking their authorization and ensuring security. MQTT suits small, cheap, low-memory and low-power devices.

## Slide 4: DDS (Data Distribution Service)
DDS is an IoT standard for real-time, scalable and high-performance machine-to-machine communication. It was developed by the Object Management Group (OMG). You can deploy DDS both in low-footprint devices and in the cloud. The DDS standard has two main layers:
• Data-Centric Publish-Subscribe (DCPS), which delivers the information to subscribers.
• Data-Local Reconstruction Layer (DLRL), which provides an interface to DCPS functionalities.

## Slide 5: XMPP (Extensible Messaging and Presence Protocol)
XMPP is a communication protocol for message-oriented middleware based on XML (Extensible Markup Language). It enables the near-real-time exchange of structured yet extensible data between any two or more network entities.

## Slide 6: Bluetooth
Bluetooth is a short-range communications technology integrated into most smartphones and mobile devices, which is a major advantage for personal products, particularly wearables. Bluetooth is well-known to mobile users. But not long ago, the new significant protocol for IoT apps appeared — Bluetooth Low-Energy (BLE), or Bluetooth Smart. This technology is a real foundation for the IoT, as it is scalable and flexible to all market innovations. Moreover, it is designed to reduce power consumption.
• Standard: Bluetooth 4.2
• Frequency: 2.4GHz band
• Range: 50-150m (Smart/BLE)
• Data Rates: 1Mbps (Smart/BLE)

## Slide 7: WiFI
Wi-Fi is the technology for wireless networking of devices. It offers fast data transfer and is able to process large amounts of data. This is the most popular type of connectivity in LAN environments.
• Standard: Based on IEEE 802.11
• Frequencies: 2.4GHz and 5GHz bands
• Range: Approximately 50m
• Data Rates: 150-200Mbps, 600 Mbps maximum

## Slide 8: Cellular
Cellular technology is the basis of mobile phone networks. But it is also suitable for the IoT apps that need functioning over longer distances. They can take advantage of cellular communication capabilities such as GSM, 3G, 4G (and 5G soon). The technology is able to transfer high quantities of data, but the power consumption and the expenses are high too. Thus, it can be a perfect solution for projects that send small amounts of information.
Standard: GSM/GPRS (2G), LTE (4G)
Frequencies: 900/1800/1900/2100MHz
Range: 35km
Data Rates: 35-170kps (GPRS), 3-10Mbps (LTE)

## Slide 9: lorawan
LoRaWAN (Long Range Wide Area Network) is a protocol for wide area networks. It is designed to support huge networks (e.g. smart cities) with millions of low-power devices. LoRaWAN can provide low-cost mobile and secure bidirectional communication in various industries.
Standard: LoRaWAN
Frequency: Various
Range: 2-5km (urban area), 15km (suburban area)
Data Rates: 0.3-50 kbps